## Slide 1
Microprocessor Design
TAs: Sebastian Giraldo, Linyan Mei,
Jasper Marien, Nathan Laubeuf

## Slide 2
Outline
Objectives of the sessions
Tools used
Architecture
Loading Programs
Exercises

## Slide 3
Objective
Design a microprocessor in RTL (Verilog) using 32 nm technology
Evaluate different microarchitectures
  Single Cycle Processor
  Single Cycle Processor
  (with Multiplication support)
  Pipelined Processor
  (without Data-Hazard resolution)
  Pipelined Processor
  (with Data-Hazard resolution)
Compare
  Performance
  Hardware Resources

## Slide 4
Objective
Single Cycle Processor
Single Cycle Processor (Multiplication support)
Pipelined Processor
Pipelined Processor (Data-Hazard resolution)
SIMULATION + SYNTHESIS
Single Cycle Processor (Not Functional)
reports
Comparison of Microarchitectures
Optimized
Pipelined Processor (Optional techniques)
Optional:

## Slide 5
Tools used
Simulation: NC Verilog (Cadence)
“Check the correctness of the hardware description implemented”
Synthesis: Design Vision (Synopsys)
“Convert a hardware description into physical gates”

## Slide 6
Tools used: Simulation
Hdl files
Testbench (cpu_tb.v)
NC Verilog
Simulation Results
Script to be loaded: incisiv_15.20.058.rc
Command used: make nc_gui or make nc

## Slide 7
Tools used: Synthesis
Design Vision
HDL files
Constraints (sdc)
Libraries (lib)
Netlist
Area/Timing/Power Reports
Scripts to load tool: synopsys_2017.09.rc
Command used: source synthesis.sh

## Slide 8
Architecture Used
Single Cycle Processor

## Slide 9
Architecture Used
cpu_tb
cpu
program_
counter
instruction_
memory
control_unit
register_file
alu_ctrl
alu
branch_unit
data_memory
regfile_dest_mux
alu_operand_mux
regfile_data_mux

## Slide 10
Architecture Used
Control unit
File: control.v

## Slide 11
Architecture Used
Register file
File: register_file.v

## Slide 12
Architecture Used
Program counter (PC)
File: pc.v
(Be careful, there is
more logic)

## Slide 13
Architecture Used
Branch unit
File: branch_unit.v

## Slide 14
Architecture Used
ALU
File: alu.v

## Slide 15
Architecture Used
ALU control
File: alu_control.v

## Slide 16
Architecture Used
Instruction memory
File: sram.v
Data memory
File: sram.v

## Slide 17
Architecture Used
Regfile_dest_mux File:mux_2.v
Alu_operand_mux File: mux_2.v
Regfile_data_mux File: mux_2.v

## Slide 18
Programs
MIPS language
2 extra instructions
  NOP (opcode: 111111)
  STOP (opcode: 111110)
5 programs
  Simple_program
  MULT1
  MULT2
  MULT3
  OPTIONAL
How to load a program?
  Go to SIM/data and modify
    Imem_content.txt
    Dmem_content.txt

## Slide 19
Programs
Functions of Testbench (cpu_tb.v)
Design Vision
Loading Data Memory
Design Vision
Loading Instr. Memory
Check
Execution
Start of Program
End
of Program
CPU
Stimulation Logic
cpu_tb
dmem_content
imem_content

## Slide 20
Programs
addi $s0, $0, 7
addi $s1, $s0, 2
sw $s1, 0($0)
lw $s2, 0($0)
add $s3, $s0, $s2
beq $s1,$s2, FINAL
add $s4, $s0, $s1
FINAL: add $s4, $s2,$s3
simple_program
a = 7
b = a + 2
save a
c = load a
d = a + c
if b != c:
e = a + b
else:
e = c + d

## Slide 21
Programs
When there is no hardware support multiplication:
1 1 0
X 1 0 1
1 1 0
0 0 0
1 1 0
1 1 1 1 0
The same as the sum of:
110 (Shifting “110” by 0 positions)
0000 (Shifting “000” by 1 position)
11000 (Shifting “110” by 2 positions)
Algorithm:
Acc = 0
N = operand1
Traverse each bit of operand2 (LSB -> MSB)
  If the bit of operand2 is 1, accumulate. Acc = Acc + N.
  If the bit is 0, Acc = Acc.
  Left shift N by 1 position.
mult1

## Slide 22
Programs
addi $16, $0, 40
addi $8, $0, 0
addi $9, $0, 0
M1: lw $17, 0($8)
lw $18, 4($8)
addi $23, $0, 32
addi $19, $0, 1
addi $20, $0, 0
add $22, $0, $17
LOOP_0: and $21, $18, $19
beq $21, $0, SHIFTING_0
It makes 5 multiplications with 10 integers.
The results are summed together.
** based on addition and shifting
add $20, $20, $22
SHIFTING_0: sll $22, $22, 1
sll $19, $19, 1
addi $23,$23,-1
beq $23, $0, M2
j LOOP_0
M2: add $9, $9, $20
addi $16, $16, -8
addi $8, $8, 8
beq $16, $0, FINISH
j M1
FINISH:
Data Memory
1
2
3
4
5
6
7
8
9
a
Instr. Memory
$16: Total size of data memory
$8: Data Memory Pointer
$9: Final result
$17: Operand 1
$18: Operand 2
$23: Iteration over the num of bits (32)
$19: 0x00000001 under left shifting (mask)
$20: Accumulated result of each partial sum
$22: Operand 1 under left shifting
$21: Current bit of operand 2
mult1

## Slide 23
Programs
lw $8, 0($0)
lw $9, 4($0)
lw $10, 8($0)
lw $11, 12($0)
lw $12, 16($0)
lw $13, 20($0)
lw $14, 24($0)
lw $15, 28($0)
lw $16, 32($0)
lw $17, 36($0)
** Using of mult instruction
addi $23, $0, 0
nop
nop
nop
add $23, $23, $18
nop
nop
nop
add $23, $23, $19
nop
nop
nop
add $23, $23, $20
nop
nop
nop
add $23, $23,$21
nop
nop
nop
add $23, $23,$22
Instr. Memory
Data Memory
1
2
3
4
5
6
7
8
9
a
mult $18, $8, $9
mult $19, $10, $11
mult $20, $12, $13
mult $21, $14, $15
mult $22, $16, $17
mult2

## Slide 24
Programs
lw $8, 0($0)
lw $9, 4($0)
lw $10, 8($0)
lw $11, 12($0)
lw $12, 16($0)
lw $13, 20($0)
lw $14, 24($0)
lw $15, 28($0)
lw $16, 32($0)
lw $17, 36($0)
** Using of mult instruction
** No NOPS between
data-dependent
instructions
addi $23, $0, 0
add $23, $23, $18
add $23, $23, $19
add $23, $23, $20
add $23, $23,$21
add $23, $23,$22
Instr. Memory
Data Memory
1
2
3
4
5
6
7
8
9
a
mult $18, $8, $9
mult $19, $10, $11
mult $20, $12, $13
mult $21, $14, $15
mult $22, $16, $17
mult3

## Slide 25
Programs
Instr. Memory
Data Memory
0
1
2
3
4
5
6
7
8
9
0
1
2
…
optional

## Slide 26
Exercise
Session 1:
      Complete Single Cycle Processor (simpleprogram, mult1)
      Add support for Multiplication (simpleprogram, mult1, mult2)
Session 2:
      Pipelined Processor (without data-hazard resolution)
      (simpleprogram, mult2)
Session 3:
      Pipelined Processor (with data-hazard resolution)
      (simpleprogram, mult2, mult3)
      [Optional] Performance Optimization (SIMD, control-hazard detection, hardware loop counter, …)
      (simpleprogram, mult2, mult3, optional)
(testing programs)

## Slide 27
REMARKS
The assignments must be completed in groups of 2 people.
Important: Make sure at least one student in a group has Verilog experience.
After completing each one of the exercises, the result must be shown to the TAs for its correspondent evaluation.
You will hand in the final version of the code together with a small report based on the template that you find in the folder. This counts for 2 points in the final H05d3A grade.
This report should be handed in through Toledo by April 10th, 2020.